## Slide 1: Penn Prime Air
Matt Schulman
Josh Pearlstein
Steffi Maiman

## Slide 2: We Have Focused on Harnessing Optics for Uber-Accurate Landing Capability
Uber-Accurate Landing
  Went forward with GPS + Optics Approach
  Designed Software System Components
    Interfacing with Drone
    Recognizing Location of QR Flag/Poster in Image
    Algorithm to Update Location of Drone
Integration of Software System Components
Testing and Refinement
Drone Routing

## Slide 3: Drone Landing Software Design Flowchart
Determine where the QR code is in the image
Determine How the Drone Should Move
Move Drone
Take New Image
Landed?
STOP
Move
Drone
Command
YES
NO
New
Image
@ New
Altitude
Location
of QR Flag

## Slide 4: QR Flag Optics Leverages OpenCV Computer Vision
OpenCV: BSD license → free for both academic and commercial use
  common infrastructure for computer vision applications
Progress: Template Matching in Java

## Slide 5
INPUTS:
Template
Source
OUTPUT:
(1142,103)

## Slide 6: The OpenCV Features2D Framework Will Make the Optics QR Flag Recognition More Robust
1st Next Step: Features2D Framework
  “Template matching...is not good when your object is rotated or scaled in scene”
  Goals with Features2D Framework
    1) Avoid worrying about expected # of pixels in QR code
    2) Handle rotated QR codes seamlessly
2nd Next Step: Java Servlet API

## Slide 7: Drone Movement Algorithm
Algorithm comprised of 3 components:
Recursive function for movement
  Uses a calculated pixel-to-foot ratio
  Drone is moved to location above QR code
  Lowers drone to proportion of altitude
  will be using an experimented zoom ratio (between 0 and 1) depending on the image quality
Landing function
  Called when the drone reaches an altitude threshold ~3-5 feet
New Image function
  Better accuracy
  Process new image at every altitude change
  Re-calculate pixel-to-foot ratio

## Slide 8: Drone Movement Algorithm Walkthrough Example
Drone Altitude: 100ft
Drone Altitude:
(100*zoomRatio) ft
Original Image:
width = x
height = y
‘Zoomed’ Image:
width = x * zoom
height = y * zoom

## Slide 9: Drone Interfacing
Currently interfacing with drone through an iPhone
  Next steps include moving that interface to drone hardware
Fully implemented all drone movement
  Adding GPS waypoints
  Full Gimbal 360 control
  Speed, altitude controls
Currently: Drone takes image sends to iPhone which sends to remotely hosted image processing server which sends results back to iPhone for control commands
Next steps: Drone takes image, processes on board, decides which commands to take

## Slide 10: High Level Next Steps
Integration of Software System Components
  Refine Optic Component
    Template Matching → Feature2D
    Rotated Images Compatibility
  Java Servlet API for Optic Component
    N64 → image conversion
    QR creation from QR code
    Possibly look into writing optics openCV algorithm in ios app to avoid API calls
  Test with Drone
    Integration pains?
    Ideal magnitude of Drone movement commands (tradeoff between speed & accuracy)
    Refinement of Drone movement algorithm
Testing and Refinement
Drone Routing